## Slide 1: UDP Performance and PCI-X Activity of the Intel 10 Gigabit Ethernet Adapter on: HP rx2600 Dual Itanium 2 SuperMicro P4DP8-2G Dual Xenon Dell Poweredge 2650 Dual Xenon
Richard Hughes-Jones Many people helped including: Sverre Jarp and Glen Hisdal CERN Open Lab Sylvain Ravot, Olivier Martin and Elise Guyot DataTAG project Les Cottrell, Connie Logg and Gary Buhrmaster SLAC Stephen Dallison MB-NG

## Slide 2
Introduction
10 GigE on Itanium IA64
10 GigE on Xeon IA32
10 GigE on Dell Xeon IA32
Tuning the PCI-X bus
SC2003 Phoenix

## Slide 3: Latency & Throughput Measurements
UDP/IP packets sent between back-to-back systems
  Similar processing to TCP/IP but no flow control & congestion avoidance algorithms
  Used UDPmon test program
Latency
  Round trip times using Request-Response UDP frames
  Latency as a function of frame size
    Slope s given by:
    Mem-mem copy(s) + pci + Gig Ethernet + pci + mem-mem copy(s)
    Intercept indicates processing times + HW latencies
  Histograms of ‘singleton’ measurements
UDP Throughput
  Send a controlled stream of UDP frames spaced at regular intervals
  Vary the frame size and the frame transmit spacing & measure:
    The time of first and last frames received
    The number packets received, lost, & out of order
    Histogram inter-packet spacing received packets
    Packet loss pattern
    1-way delay
    CPU load
    Number of interrupts
Tells us about:
  Behavior of the IP stack
  The way the HW operates
  Interrupt coalescence
Tells us about:
  Behavior of the IP stack
  The way the HW operates
  Capacity & Available throughput of the LAN / MAN / WAN

## Slide 4: The Throughput Measurements
UDP Throughput
Send a controlled stream of UDP frames spaced at regular intervals
Zero stats
OK done
●●●
Get remote statistics
Send statistics:
No. received
No. lost + loss pattern
No. out-of-order
CPU load & no. int
1-way delay
Send data frames at
regular intervals
●●●
Time to send
Time to receive
Inter-packet time
(Histogram)
Signal end of test
OK done
n bytes
Number of packets
Wait time
time


## Slide 5: The PCI Bus & Gigabit Ethernet Measurements
PCI Activity
Logic Analyzer with
  PCI Probe cards in sending PC
  Gigabit Ethernet Fiber Probe Card
  PCI Probe cards in receiving PC
Gigabit
Ethernet
Probe
CPU
mem
chipset
NIC
CPU
mem
NIC
chipset
Logic Analyser
Display

## Slide 6: Example: The 1 Gigabit NIC Intel pro/1000
Latency
Throughput
Bus Activity
Motherboard: Supermicro P4DP6
Chipset: E7500 (Plumas)
CPU: Dual Xeon 2 2GHz with 512k L2 cache
Mem bus 400 MHz PCI-X 64 bit 66 MHz
HP Linux Kernel 2.4.19 SMP
MTU 1500 bytes
Intel PRO/1000 XT
Receive Transfer
Send Transfer

## Slide 7: Data Flow: SuperMicro 370DLE: SysKonnect
Motherboard: SuperMicro 370DLE Chipset: ServerWorks III LE Chipset
CPU: PIII 800 MHz PCI:64 bit 66 MHz
RedHat 7.1 Kernel 2.4.14
1400 bytes sent
Wait 100 us
~8 us for send or receive
Stack & Application overhead ~ 10 us / node
Send PCI
Receive PCI
~36 us
Send Transfer
Send CSR setup
Receive Transfer
Packet on Ethernet Fibre

## Slide 8: 10 Gigabit Ethernet NIC with the PCI-X probe card.

## Slide 9: Intel PRO/10GbE LR Adapter in the HP rx2600 system

## Slide 10: 10 GigE on Itanium IA64: UDP Latency
Motherboard: HP rx2600 IA 64
Chipset: HPzx1
CPU: Dual Itanium 2 1GHz with 512k L2 cache
Mem bus dual 622 MHz 4.3 GByte/s
PCI-X 133 MHz
HP Linux Kernel 2.5.72 SMP
Intel PRO/10GbE LR Server Adapter
NIC driver with
  RxIntDelay=0
  XsumRX=1 XsumTX=1
  RxDescriptors=2048 TxDescriptors=2048
MTU 1500 bytes
Latency 100 µs & very well behaved
Latency Slope 0.0033 µs/byte
B2B Expect: 0.00268 µs/byte
  PCI 0.00188 **
  10GigE 0.0008
  PCI 0.00188
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 11: 10 GigE on Itanium IA64: Latency Histograms
Double peak structure with the peaks separated by 3-4 µs
Peaks are ~1-2 µs wide
Similar to that observed with 1 Gbit Ethernet NICs on IA32 architectures
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 12: 10 GigE on Itanium IA64: UDP Throughput
HP Linux Kernel 2.5.72 SMP
MTU 16114 bytes
Max throughput 5.749 Gbit/s
Int on every packet
No packet loss in 10M packets
Sending host, 1 CPU is idle
For 14000-16080 byte packets, one CPU is 40% in kernel mode
As the packet size decreases load rises to ~90% for packets of 4000 bytes or less.
Receiving host both CPUs busy
16114 bytes 40% kernel mode
Small packets 80 % kernel mode
TCP gensink data rate was 745 MBytes/s = 5.96 Gbit/s
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 13: 10 GigE on Itanium IA64: UDP Throughput [04]
HP Linux Kernel 2.6.1 #17 SMP
MTU 16114 bytes
Max throughput 5.81 Gbit/s
Int on every packet
Some packet loss pkts < 4000 bytes
Sending host, 1 CPU is idle – but swap over
For 14000-16080 byte packets, one CPU is 20-30% in kernel mode
As the packet size decreases load rises to ~90% for packets of 4000 bytes or less.
Receiving host 1 CPU is idle – but swap over
16114 bytes 40% kernel mode
Small packets 70 % kernel mode
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 14
16080 byte packets every 200 µs Intel PRO/10GbE LR Server Adapter MTU 16114
setpci -s 02:1.0 e6.b=2e (22 26 2a ) mmrbc 4096 bytes (512 1024 2048)
PCI-X Signals transmit - memory to NIC
Interrupt and processing: 48.4 µs after start
Data transfer takes ~22 µs
Data transfer rate over PCI-X: 5.86 Gbit/s
10 GigE on Itanium IA64: PCI-X bus Activity
CSR Access
Transfer of 16114 bytes
PCI-X bursts 256 bytes
Made up of 4 PCI-X sequences of ~4.55 µs then a gap of 700 ns
Sequence contains 16 PCI bursts 256 bytes
Sequence length 4096 bytes ( mmrbc)
CSR Access
PCI-X Sequence 4096 bytes
PCI-X bursts 256 bytes
Gap 700ns
PCI-X Sequence

## Slide 15
16080 byte packets every 200 µs Intel PRO/10GbE LR Server Adapter MTU 16114
setpci -s 02:1.0 e6.b=2e (22 26 2a ) mmrbc 4096 bytes (512 1024 2048)
PCI-X Signals transmit - memory to NIC
Interrupt and processing: 48.4 µs after start
Data transfer takes ~22 µs
Data transfer rate over PCI-X: 5.86 Gbit/s
PCI-X Signals receive – NIC to memory
Interrupt every packet
Data transfer takes ~18.4 µs
Data transfer rate over PCI-X : 7.014 Gbit/s
Note: receive is faster cf the 1 GE NICs
10 GigE on Itanium IA64: PCI-X bus Activity
CSR Access
Transfer of 16114 bytes
PCI-X bursts 256 bytes
Interrupt
CSR Access
Transfer of 16114 bytes
PCI-X bursts 512 bytes
PCI-X Sequence

## Slide 16: 10 GigE on Xeon IA32: UDP Latency
Motherboard: Supermicro P4DP8-G2
Chipset: Intel E7500 (Plumas)
CPU: Dual Xeon 2.2GHz with 512k L2 cache
Mem bus 400 MHz
PCI-X 133 MHz
RedHat Kernel 2.4.21 SMP
Intel(R) PRO/10GbE Network Driver v1.0.45
Intel PRO/10GbE LR Server Adapter
NIC driver with
  RxIntDelay=0
  XsumRX=1 XsumTX=1
  RxDescriptors=2048 TxDescriptors=2048
MTU 1500 bytes
Latency 144 µs & reasonably behaved
Latency Slope 0.0032 µs/byte
B2B Expect: 0.00268 µs/byte
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 17: 10 GigE on Xeon IA32: Latency Histograms
Double peak structure with the peaks separated by 3-4 µs
Peaks are ~1-2 µs wide
Simliar to that observed with 1 Gbit Ethernet NICs on IA32 architectures
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 18: 10 GigE on Xeon IA32: Throughput
MTU 16114 bytes
Max throughput 2.75 Gbit/s mmrbc 512
Max throughput 3.97 Gbit/s mmrbc 4096 bytes
Int on every packet
No packet loss in 10M packets
Sending host,
For closely spaced packets, the other CPU is ~60-70 % in kernel mode
Receiving host
Small packets 80 % in kernel mode
>9000 bytes ~50% in kernel mode
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 19: 10 GigE on Xeon IA32: PCI-X bus Activity
16080 byte packets every 200 µs Intel PRO/10GbE LR mmrbc 512 bytes
PCI-X Signals transmit - memory to NIC
Interrupt and processing: 70 µs after start
Data transfer takes ~44.7 µs
Data transfer rate over PCI-X: 2.88Gbit/s
PCI-X Signals receive – NIC to memory
Interrupt every packet
Data transfer takes ~18.29 µs
Data transfer rate over PCI-X : 7.014Gbit/s same as Itanium
Interrupt
CSR Access
Transfer of 16114 bytes
PCI-X burst 256 bytes
Interrupt
Transfer of 16114 bytes
CSR Access

## Slide 20: 10 GigE on Dell Xeon: Throughput
MTU 16114 bytes
Max throughput 5.4 Gbit/s
Int on every packet
Some packet loss pkts < 4000 bytes
Sending host,
For closely spaced packets, one CPU is ~70% in kernel mode
CPU usage swaps
Receiving host
1 CPU is idle but CPU usage swaps
For closely spaced packets ~80 % in kernel mode
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 21: 10 GigE on Dell Xeon : UDP Latency
Motherboard: Dell Poweredge 2650
Chipset: Intel E7500 (Plumas)
CPU: Dual Xeon 3.06 GHz with 512k L2 cache
Mem bus 533 MHz
PCI-X 133 MHz
RedHat Kernel 2.4.20 altAIMD
Intel(R) PRO/10GbE Network Driver v1.0.45
Intel PRO/10GbE LR Server Adapter
NIC driver with
  RxIntDelay=0
  XsumRX=1 XsumTX=1
  RxDescriptors=2048 TxDescriptors=2048
MTU 16114 bytes
Latency 36 µs with some steps
Latency Slope 0.0017 µs/byte
B2B Expect: 0.00268 µs/byte
Notes: Dual Itanium 2 1GHz with 512k L2 cache

## Slide 22: 10 GigEthernet: Throughput
1500 byte MTU gives ~ 2 Gbit/s
Used 16144 byte MTU max user length 16080
DataTAG Supermicro PCs
Dual 2.2 GHz Xeon CPU FSB 400 MHz
PCI-X mmrbc 512 bytes
wire rate throughput of 2.9 Gbit/s
SLAC Dell PCs giving a
Dual 3.0 GHz Xeon CPU FSB 533 MHz
PCI-X mmrbc 4096 bytes
wire rate of 5.4 Gbit/s
CERN OpenLab HP Itanium PCs
Dual 1.0 GHz 64 bit Itanium CPU FSB 400 MHz
PCI-X mmrbc 4096 bytes
wire rate of 5.7 Gbit/s

## Slide 23
Tuning PCI-X: Variation of mmrbc IA32
mmrbc
1024 bytes
mmrbc
2048 bytes
mmrbc
4096 bytes
mmrbc
512 bytes
CSR Access
PCI-X Sequence
Data Transfer
Interrupt & CSR Update
16080 byte packets every 200 µs
Intel PRO/10GbE LR Adapter
PCI-X bus occupancy vs mmrbc
Plot:
  Measured times
  Times based on PCI-X times from the logic analyser
  Expected throughput

## Slide 24: Tuning PCI-X: Throughput vs mmrbc
DataTag IA32
2.2 GHz Xeon
400 MHz FSB
2.7 – 4.0 Gbit.s
SLAC Dell
3.0 GHz Xeon
533 MHz FSB
3.5 - 5.2 Gbit/s
OpenLab IA64
1.0 GHz Itanium
622 MHz FSB
3.2 - 5.7 Gbit/s
CPU load is 1 CPU not average

## Slide 25: 10 GigEthernet at SC2003 BW Challenge
Three Server systems with 10 GigEthernet NICs
Used the DataTAG altAIMD stack 9000 byte MTU
Send mem-mem iperf TCP streams From SLAC/FNAL booth in Phoenix to:
  Pal Alto PAIX
  rtt 17 ms , window 30 MB
  Shared with Caltech booth
  4.37 Gbit hstcp I=5%
  Then 2.87 Gbit I=16%
  Fall corresponds to 10 Gbit on link
  3.3Gbit Scalable I=8%
  Tested 2 flows sum 1.9Gbit I=39%
  Chicago Starlight
  rtt 65 ms , window 60 MB
  Phoenix CPU 2.2 GHz
  3.1 Gbit hstcp I=1.6%
  Amsterdam SARA
  rtt 175 ms , window 200 MB
  Phoenix CPU 2.2 GHz
  4.35 Gbit hstcp I=6.9%
  Very Stable
  Both used Abilene to Chicago

## Slide 26
Summary & Conclusions
Intel PRO/10GbE LR Adapter and driver gave stable throughput and worked well
Need large MTU (9000 or 16114) – 1500 bytes gives ~2 Gbit/s
PCI-X tuning mmrbc = 4096 bytes increase by 55% (3.2 to 5.7 Gbit/s)
PCI-X sequences clear on transmit gaps ~ 950 ns
Transfers: transmission (22 µs) takes longer than receiving (18 µs)
Tx rate 5.85 Gbit/s Rx rate 7.0 Gbit/s (Itanium) (PCI-X max 8.5Gbit/s)
CPU load considerable 60% Xenon 40% Itanium
BW of Memory system important – crosses 3 times!
Sensitive to OS/ Driver updates
More study needed

## Slide 28: Test setup with the CERN Open Lab Itanium systems

## Slide 29: 1 GigE on IA32: PCI bus Activity 33 & 66 MHz
1472 byte packets every 15 µs Intel Pro/1000
PCI:64 bit 33 MHz
82% usage
PCI:64 bit 66 MHz
65% usage
Data transfers half as long
Send PCI
Receive PCI
Send setup
Data Transfers
Receive Transfers
Send PCI
Receive PCI
Send setup
Data Transfers
Receive Transfers